## Slide 1: C P U
8
Addressing Mode

## Slide 2: Addressing Modes
The operation field of an instruction specifies the operation to be performed.
This operation must be executed on some data stored in registers or memory word.

## Slide 3
The way the operands are chosen during the program execution depends on the addressing mode of the instruction.
Addressing mode is a rule for modifying the address field of the instruction before the operand is actually referenced.

## Slide 4
Every instructions involves one or more operands. The operand may be processor register, constants or memory word.
Ex. ADD R1,R2
AND M[100],R3
ADD 50 // AC AC+50
ADD B // AC  AC + B
The way an instruction references its operands is called its addressing mode.

## Slide 5
There are two modes that need no address fields at all.
These are called the implied and immediate modes.

## Slide 6: 1.Implied mode
In this mode, the operands are specified implicitly in the definition of the instruction.
All register reference instructions that uses accumulator are implied-mode instructions.

## Slide 7
Example
Zero-address instruction in a stack-organized computer are implied-mode instructions since the operands are implied to be on the top of the stack.
PUSH A
PUSH B
ADD

## Slide 8: 2.Immediate Mode
In this mode the operand is specified in the instruction itself.
An immediate mode instruction has an operand field rather than an address field.

## Slide 9
The operand field contains the actual operand value to be used in conjunction with the operation specified in the instruction.
For e.g. the instruction
ADD 10 //AC AC +10

## Slide 10: 3.Register Mode
When the address field specifies a processor register, the instruction is said to be in the register mode.
In this mode, the operands are in the registers that resides within the CPU.

## Slide 11
In general, the register addressing mode is the most efficient because registers are the part of the CPU and no memory reference is need.

## Slide 12
Examples of Register Address mode:
ADD R1 R2 // R1R1+R2
MUL AX, CX //AX AX*CX
100
200
AX
BX
300
AX
+

## Slide 13: Register Addressing Diagram
Register Address R
Opcode
Instruction
Registers
Operand
Notes: 12

## Slide 14: 4.Register Indirect Mode
In this mode, the instructions specifies a register in the CPU whose contents give the address of the operand in memory.
In other words, the selected register contains the address of the operand in memory rather than the operand itself.

## Slide 15: Register Indirect Addressing Diagram
Register Address R
Opcode
Instruction
Memory
Operand
Pointer to Operand
Registers
10
11
9
Operand
Notes: 14

## Slide 16: 5. Autoincrement or Autodecrement Mode
This is similar to register indirect mode except that the register is incremented or decremented after or before its value is used to access memory.

## Slide 17
This is achieved by using the increment and decrement instructions.

## Slide 18: 6. Direct Address Mode
In this mode, the effective address is equal to the address part of the instruction.
The operand resides in memory and its address is given directly by the address field of the instruction.

## Slide 19: 7. Indirect Address Mode
In this mode the address field of the instruction gives the address where the effective address is stored in memory.
Control fetches the instruction from the memory and uses its address part to access memory again to read the effective address.

## Slide 20: Indirect Addressing Diagram
Address A
Opcode
Instruction
Memory
Operand
Pointer to operand
Notes: 9

## Slide 21: 8. Relative Address Mode
In this mode the content of the program counter is added to the address part of the instruction in order to get the effective address.
Effective Address = Content of PC + Address of instruction.

## Slide 22
The address part of the instruction is usually a signed number (in 2’s complement notation) which can either be positive or negative.
When this number is added to the content of PC, the result produces an effective address.

## Slide 23: 9.Indexed Addressing Mode
In this mode the content of an index register is added to the address part of the instruction to obtain the effective address.
The index register is a special CPU register that contains the index value.

## Slide 24
The address field of the instruction defines the beginning address of a data array in memory.
The distance between the beginning address and the address of the operand is called the index value stored in the index register.

## Slide 25: 10.Base Register Addressing Mode
In this mode the content of a base register is added to the address part of the instruction to obtain the effective address.
This is similar to the indexed addressing mode except that the register is now called a base register instead of an index register.

## Slide 26
END